## Slide 1: A Very Forward Proton Spectrometer for H1
Pierre Van Mechelen
Universiteit Antwerpen (UIA)

## Slide 2: Participating Groups
University of Antwerp (UIA), Belgium
T. Anthonis, E. A. De Wolf, P. Van Mechelen
Inter-University Institute for High Energies (ULB-VUB),
Brussels, Belgium
L. Favart, X. Janssen, D. Johnson, P. Marage, R. Roosen
University of Hamburg II, Germany
V. Blobel, F. Büsser, V. Jemanov, A. Meyer, B. Naroska,
F. Niebergall, J. Schütt, H. Spitzer, R. van Staa
University of Lund, Sweden
L. Jönsson, H. Jung, U. Mjörnmark
University of Birmingham, UK
P. Newman

## Slide 3: Diffraction Physics at HERA
HERA I (1992-2000):
  large fraction (~10%) of “large rapidity gap” events
  strong theoretical interest (understanding in QCD)
  measurements of F2D, incl. final states, jets, charm, excl. VM
  results: soft/hard transition, gluon dominance, DGLAP consistency
  limitations: rapidity gap selection yields large systematic errors, low statistics, limited t and  measurement
HERA II (2001-2006):
  major upgrade of the H1 detector
  high luminosity regime  need for efficient VFPS-trigger
  need for clean selection by tagging the scattered proton
  need for measurement of proton momentum (xIP , t, )

## Slide 4: The H1 Forward Proton Spectrometer
Horizontal stations:
  at 60 m and 80 m from I.P.
  acceptance of a few % at high |t | and low xIP
Vertical stations:
  at 81 m and 90 m from I.P.
  large acceptance at low |t | and large xIP
Measurement of F2LP:

## Slide 5: VFPS Location
VFPS location is optimised for acceptance  220m NL
Proton beam is approached horizontally (use HERA bend)
Bypass is needed to re-route the cold beam line
xIP = 0.01
H1
ZEUS
VFPS
HERMES
HERA-B
present FPS
VFPS

## Slide 6: Bypass of Cold Beam Line
Cold section HPNL-220:
  modification of 10 m drift segment with easy access
  p -beam above e -beam
  horizontal bypass for helium and superconductor lines
  new (warm) beam pipe

## Slide 7: VFPS Detectors
VFPS detectors similar to FPS:
  2 “Roman Pot” stations equipped with 2 scintillating fibre detectors each
  1 fibre detector measures both u - and v - co-ordinates
5 fibres/light guide  8.2 photo-electrons  99.4% detection efficiency
Staggered fibres properties:

## Slide 8: Triggering Diffractive DIS at HERA-II
HERA-I strategy:
  inclusive trigger based on backward calorimeter (SPACAL) and vertex requirement (MWPC)
  off-line rapidity gap selection
HERA-II:
  factor 5 increase in luminosity
  factor 2 increase in beam currents
  inclusive triggers are pre-scaled
Rapidity gap trigger unfeasible
Level-1 VFPS trigger needed
SPACAL/MWPC trigger rates:
(V)FPS trigger rates:
coincidence rates:

## Slide 9: Simulation Studies
Linear beam transport:
Non-linear corrections:
  non-linear effects in energy deviation xIP
  sextupoles
  offset, tilted magnets
diffractive
ep scattering
beam spread
and divergence at I.P.
position, slope and
energy at VFPS
beam optic
transport matrix

## Slide 10: Acceptance
Simulation includes detailed description of beam pipe
HERA machine crew agreed to steer proton beam away from critical acceptance loss
Detectors approach beam up to “12-sigma” from inside HERA ring + 3 mm “coasting beam margin”
Acceptance range:

## Slide 11: Reconstruction
Reconstruction fit: where cij is a covariance matrix containing:
  beam covariance
  fibre detector resolution

## Slide 12: Resolution
Resolution is dominated by beam covariance (but still sensitive to fibre detector resolution)
xIP resolution is competitive with reconstruction of xIP by H1
~ 4 bins in |t |
~ 15 bins in  for |t | > 0.2 GeV2

## Slide 13: Alignment
Relative positioning of detectors versus nominal proton beam
Exploit kinematic peak and xIP -measurement by H1
Calibration fit:
Alignment precision of ~100 m is feasible
Alternative fits are possible with e.g. elastic  mesons

## Slide 14: Expected Results
Inclusive diffraction:
  luminosity: 350 pb-1 (3 years of HERA-II running, 50% VFPS operation efficiency)
  test of hard scattering fact.: F2D (, Q 2) at fixed xIP , |t |
  uncorrelated systematic errors can approach the level of F2 (few %)
  event yields:

## Slide 15: Expected Results
Hadronic final states:
  Open charm production:
    1996/97 D* analysis yielded 4610 ev.
    full HERA-I data sample: factor 2-3
    HERA-II/VFPS expectation: 380 ev.
  Diffractive dijet electroproduction:
    1996/97 dijet analysis yielded 2500 ev.
    HERA-II/VFPS expectation: 22900 ev.
  Diffractive dijet photoproduction:
    HERA-II/VFPS expectation:
    eTag-6 (W = 275 GeV): 1400 ev.
    eTag-40 (W = 140 GeV): 20000 ev.
open charm production
dijet electroproduction

## Slide 16: Expected Results
Azimuthal asymmetry
  angle between proton and electron scattering planes () gives a handle on T and L and their interference terms:
  15 bins with each 10,000 events!
  study asymmetry as a function of , Q 2
Deeply Virtual Compton Scattering
  only 25 DVCS observed in 1997
  HERA-II/VFPS expectation: 3600 events (Q 2 > 8 GeV2)
  VFPS adds to H1-triggered DVCS, mostly at low W, low Q 2

## Slide 17: Conclusion
Timeline
VFPS mandatory to trigger diffraction at HERA-II
Very good acceptance in narrow window around xIP = 0.01
Good resolution on reconstructed proton momentum will allow exciting physics analyses
DESY-PRC approved the project in October 2001
Bypass and VFPS construction are on schedule
Insertion in HERA machine is foreseen for early 2003 shutdown
Data taking from 2004 to 2006...